HT-1600( R )-PCI

Dyno Data Acquisition Software

Since 1989, Huff Technologies Inc. has been building data acquisition systems for all types of dynamometer testing.  From NASCAR V-8’s to one(1) cylinder go-carts, Huff Technologies Inc. has instrumented  water brakes, and hydraulic brakes to provide the most repeatable and informative dyno systems in the business.

Huff Technologies Inc.  dyno data acquisition systems are PC based and run under a Windows 95/98/2000 operating system.  They include one(1) data acquisition card which mounts in any PCI slot in your PC.  All cables are provided to your specified length for your convenience.

Systems Requirements:

IBM( Compatible PC w/Pentium II ( 633 processor and 32 MB Memory

Water Brake, Hydraulic, or Eddy Current dynamometer w/ Torque cell or pressure output.

Power Requirements:  120vac @ 10 Amps (standard wall outlet)

Features:

Real time Inertia Compensation

Calculation of :  Correction factor, Brake Specific Fuel Consumption ,Air density, volumetric efficiency, Fuel flow, mass air flow, CFM, SCFM, Acceleration Rate, and # Samples.

User Calibration of all sensors

Real Time Graphing during Run

Print, Plot, Store, and retrieve  all data

HUFF Technologies Inc.

325 Industrial Rd.  Morganfield,  KY  42437

ph:  270.389.4833  fx: 270.389.4831

e-Mail:  dhuff@huff-tech.com

Web:  www.huff-tech.com

Engine Dynamometers

Specifications:

The standard system includes:

Sixteen (16) Analog Sensor Inputs with programmable ranges.  Nine(9) of the fourteen are dedicated to: Torque, RPM, air temp, humidity, barometer, Fuel Flow1, Fuel Flow2, Mass Airflow1, Mass Airflow2, three(3) EGT’s, and two(2) Low Temp Probes  .  The additional two(2) are user programmable.

Sensors Included:  Strain Gage, RPM Pick-Up, Air Temp, Relative Humidity, Barometer, and one(1) Fuel Flow Meter (specify ranges)

Huff Technologies Inc. Windows tm based “WinDyno” software with visual gauges and mouse driven pull down menus.

Technical support

Options:

Air Flow Meters (Mass or Turbine)

Additional Sensors(Pressure, Vacuum, Flow, Etc.)

Thermocouples / Adapters

Custom Software