memorandum

to:		professor kney

from:		group 3

date:		February 14, 2002

subject:	notes from site visit on february 12, 2002

1.	Tour of pool, pool building, and pump house

- Pool building is in fairly good shape, except for the bathrooms, which need a bit of work

- The green tint in the building is a bit disconcerting

- The pool is 12 feet deep at its deepest point

- The pool has one diving board

- According to Mr. Richard Barbadora, 70-80% of the people who use the pool are from outside Alpha Borough

- At one time, the pool used gaseous chlorine, but it now uses a liquid hypochlorous solution

2.	Tour of wrestling building

- Building contains 3 main rooms: a kitchen, a mat area, and a weight-lifting area

- The building also has storage closets for football and baseball equipment

- This building was built by the residents of Alpha.  Most of the materials were donated by townspeople.

3.	Soil test pits

- 2 pits were dug:

- 1 at the yard waste area (486442E, 4500651N)

- 1 next to the field house (486576E, 4500977N)

- Refer to the field notes showing the soil strata and soil descriptions

4.	Hydrology issues

- According to Mr. Richard Barbadora, the road next to the property never floods

- According to Doug, the water treatment plant now has a pH meter in the lime pit, and the plant is attempting to neutralize the chemicals before releasing them into the environment

- We drove by the houses that flood during major storm events, and we saw the farmer’s field that gets most of the flooding

- There are 2 pipes that pass under the dirt road at the farm downstream of the site:

-	Corrogated metal: 18.5”

-	Cast iron 22” ( concrete 24”

- Further downstream, there is a box culvert under the road with dimensions of 12’ x 4’

5.	Water quality

- One water sample was taken at coordinates (486670E, 4500900N)

- A second sample will be taken during a storm event