## Field Results for Bushkill Stream Study – October 17, 2005

| Morning and Afternoon LAB | Jacobsburg (Station 6) | Tatamy – Station 4 | Between Stations 3 and 2 | 22 Overpass (Just upstream of Station 1) |
| --- | --- | --- | --- | --- |
| pH | 6.811 | 7.534 | 7.739 | 7.992 |
| Alkalinity (mg/L as CaCO3) | 60 | 110 | 120 | 160 |
| Turbidity (NTU) | .90 | 5.41 | 4.54 | 3.42 |
| DO (mg/L as O2) | 9.80 | 8.15 | 11.03 | 8.58 |
| Conductivity (uS/cm) | 165 | 355 | 392 | 445 |
| Temperature (o C) | 11.8 oC | 12.9 oC | 14.0 oC | 14.3 oC |
| Macroinvertebrate | 3 May Fly 1 Snail 3 Stone Fly 4 Larva | 120 Caddis Fly 3 Beetle Larva 4 Aquatic Worm 18 May Fly 23 Stone Fly 1 Alder Fly 1 Scud | 81 Caddis Fly 4 May Fly 1 Beetle Larva 1 Leach | 9 Caddis Fly 1 Caddis Fly Larva 1 Water Penny 4 Scud |
| TC Test (# of col./100 ml) 0 dilution/10 x dilution | 7200 colonies/100 ml | 1620 colonies/100 ml | 4800 colonies/100 ml | 1530colonies/100 ml |