# Coliform Summary Sheet

Coliforms are indicator organisms used to alert water uses that there may be a type of contamination that can lead to sickness and possibly even death.  Coliforms are made of the following genera found in the family Enterobacteriacae.

Not all member of the Family Enterobacteriacae are Coliforms

Properties of Coliforms

- Gram negative  (a staining technique)

- Bacillus (rod shaped)

- Facultative anaerobes (can exist in an environment with no oxygen)

- Non-spore forming

Drinking water standards based on Total Coliform (TC) test.

No more than 5% of 40 or more samples/month can be positive, if less than 40 samples taken in one month then no more than 1 sample can be positive

Every sample containing TC must be analyzed for Fecal Coliform (FC – indicator organism is Escherichia Coliform or E. Coli.).

TC = Warm blooded Animals; FC Warm blooded Mammals

MCLG for TC and FC is 0.

If FC is positive and/or TC greater than 5% (or 1 in 40 or less) than action must be taken to address the issue.

TC test done at 35oC; FC test done at 44.5oC

Recreational Area Standards based on TC test.

TC test must show less than 1000 coliform/100 ml

Coliforms reported as # of colonies per 100 milliliter of sample

Produced by David Kendall, Ryan Clark and RJ Sindelar