memorandum

to:		professor kney

from:		group 3

date:		april 13, 2002

subject:	agenda for group meeting on april 12, 2002

1.	Announcements/updates from Professor Kney

- As noted on the syllabus, we will have a practice run of our presentation on the Monday before we present at Alpha.

- Next week we should bring to our group meetings an outline of each section of the report.

- Our final report is now due on Thursday, May 9, rather than Friday, May 10.

- We can make copies at Lehigh Blue or Sir Speedy.

2.	Comments on deliverables:

- Drainage plan

-	We will probably need a catch basin at the corner of the building.

-	We should show some spot elevations on the drawing.

-	The pipe under the road next to the playground is a good idea.

-	Normally sumps would not be used.

-	New Jersey uses the Barrier-free design code, which mimics the ADA code, but is slightly stricter.  We should be aware of this fact.

-	For the detention basin, we must be careful of the property boundaries.  We may need to add a small earthen embankment to keep to the water off neighboring properties.

-	For the “dam”, we should design an emergency spillway with huge riprap.  This emergency spillway will only kick in for the 50-year storm.

-	The “dam” should be constructed of concrete or riprap – not dirt.

-	We may want to widen the “dam”.

-	We are allowed to fill up to 20% of the area in between the floodway and the floodplain.

-	For the water quality basin, we may want to consider using a v-notch weir with 3-inch orifices.  V-notch weirs have excellent control characteristics and are easy to construct.

- Elevation drawings

- Stream cross sections

-	Presented very well.

- Transportation study

- Rough draft of ESA report

3.	Updates / plans for future work:

- Structures

-	SAP model is running

-	Has column loads and moments

-	Plans to check beams and columns with highest loads to make sure SAP is giving accurate results

- Geotech

-	Will begin foundation design this week

- Transportation

-	Traffic study is complete

-	Plan to investigate ways to improve intersection (striping/realignment)

- Site Work / Site Hydrology

-	See above

- Environmental

-	Rough draft of ESA report is done

- Hydrology

-	Has started making stream encroachment plans

-	Will add floodplain/floodway to cross-sections

-	Trying to run PondPak