memorandum

to:		professor kney

from:		group 3

date:		April 2, 2002

subject:	meeting minutes from group meeting on march 22, 2002

- Announcements/updates from Professor Kney:

- Week after spring break (Friday April 12th) Doug and Paul will be attending the meeting. Structures should have one profile of the building complete.

- After talking with Doug Professor Kney felt we should reconsider the idea of an online detention basin

- Suggestions made by Professor Ruggles about the current drainage plans:

- Use swale to collect runoff from tennis court area, rather then using underground piping for reasons of cost efficiency.

- Slope parking lot with grading rather then using underground pipes will also help reduce costs. Make sure lowest parking lot elevation is lower then finished floor elevation.

- Use of openings in curb to direct storm runoff.

3.	Comments regarding emergency spillway for regional detention basin:

- Constructed embankment will need either grass or crushed rock on downstream side, to control flow passing over the embankment directed to a channel.

- Soil samples are needed at the embankment area in order to test for permeability.