# Lafayette College

Department of Civil and Environmental Engineering

CE 321: Introduction to Environmental Engineering and Science	Fall 2019

Homework #10

Due: Monday, 11/25/19

- If the BOD of a municipal wastewater at the end of 7 days is 60 mg/L and the ultimate BOD is 85.0 mg/L, what is the rate constant?

- Assuming that the data in Problem 1 were taken at 25oC, computer the rate constant at 16oC.

- A sample of municipal sewage is diluted to 1% by volume prior to running a BOD5 analysis.  After 5 days the oxygen consumption is determined to be 2.00 mg/L.   What is the BOD5 of the sewage?

- If the BOD5 values for two livestock wastes having k values of 0.3800 day-1 and 0.240 day-1 are16230.0 mg/L, what would be the ultimate BOD for each?

- A wastewater has a five-day BOD equal to 210 mg/L (test performed at 20oC) and an ultimate BOD of 350 mg/L.  Find the five-day BOD at 25oC.

- In a standard five-day BOD test,

  - Why is the BOD bottle stoppered?

  - Why is the test run in the dark (or in a black bottle)?

  - Why is it usually necessary to dilute the sample?

  - Why is it sometimes necessary to seed the sample?

  - Why isn’t ultimate BOD measured?

  - What concentration of DO would you suggest as a starting concentration.

- Assuming 0.1 mM of glutamic acid (C5H9O4N) is used in the following stoichiometric reactions, calculate the Theoretical NBOD of glutamic acid.

C5H9O4N + 4.5O2 ( 5CO2 + 3H2O + NH3

NH3 + 2O2 ( NO3- + H+ + H2O

- If the dissolved oxygen concentration measured during a BOD test is 9 mg/L initially, 6 mg/L after 5 days, and 3 mg/L after an indefinitely long period of time, calculate the 10-day BOD.

- The following figure shows a plot of BOD remaining versus time for a sample of the effluent taken from a wastewater treatment plant.

  - What is the ultimate BOD (Lo)?

  - What is the five-day BOD?

  - What is Lt for 7 days?

- If the BOD5 for some wastewater if 200 mg/L and the ultimate BOD is 300 mg/L, find the reaction rate constant k (base e) and K (base 10).

- Suppose a wastewater has a BOD5 equal to 180 mg/L and a reaction rate (k) equal to 0.22/day.

  - Find the ultimate carbonaceous oxygen demand (CBOD).

  - Find the remaining BOD after five days have elapsed.

- Glutamic acid (C5H9O4N) is used as one of the regent for a standard to check the BOD test.  Determine the theoretical oxygen demand of 150 mg/L of glutamic acid.  Assuming the following reactions:

C5H9O4N + 4.5O2 ( 5CO2 + 3H2O + NH3

NH3 + 2O2 ( NO3- + H+ + H2O

- 10.0 ml sample of wastewater with enough water to fill a 300 ml bottle has an initial DO of 9.0 mg/L.  To help assure an accurate test, it is desirable to have at least a 2.0 mg/L drop in DO during the five day run, and the final DO should be at least 2 mg/L.  For what range of BOD5 would this dilution produce the desired results.  Assume this test to be a five-day, unseeded BOD test.

- A water sample is diluted by a factor of 10 using seeded dilution water. Dissolved oxygen concentration is measured at 1-d intervals, and the results are listed below.  Using these data, determine the BOD as a function of time, i.e., calculate the BOD for each day.

| Time, d | Diluted Sample Dissolved Oxygen, g/m3 | Seeded Blank Dissolved Oxygen, g/m3 |
| --- | --- | --- |
| 0 | 8.55 | 8.75 |
| 1 | 4.35 | 8.70 |
| 2 | 4.05 | 8.66 |
| 3 | 3.35 | 8.61 |
| 4 | 2.75 | 8.57 |
| 5 | 2.40 | 8.53 |
| 6 | 2.10 | 8.49 |
| 7 | 1.85 | 8.46 |